## Slide 1: MicroWIP325: A Low-Area Architectural Design and Analysis of Processors for Wearable Technologies.
INTERNATIONAL CONFERENCE ON COMMUNICATION, COMPUTING AND INTERNET OF THINGS
IC3IoT 2022
PAPER ID: IC3IoT22128
AUTHORS:
Dr. Arthi R.
Benjamin George Samuel
Deepak Shankar R.
Aparnna Ajay
SRM Institute of Science & Technology
Ramapuram - Chennai

## Slide 2: CONTENTS
Abstract
Introduction
System Architecture
Hardware Design and Development
Conclusion and Future Scope

## Slide 3: ABSTRACT
With the rise of smart wearables came the need for very high processing power built into devices of small area as the size of your wrist.
MicroWIP325 stands for 32-bit Microprocessor Without Interlocked 5 - Pipelines.
As of April 2017, MIPS32 Release 6 Architecture is existent and several authors have implemented this architectural design and also previous releases of MIPS in Field Programmable Gate Arrays (FPGA) such as Spartan – 03E, Spartan – 6.
Through this paper we are focusing on the feasibility of hardware execution within the design space requirements of Xilinx Spartan – 07 (XC7S100-676FGGA-2) FPGA and Intel Cyclone V-E (5CEFA7F31C8N) FPGA, both of which are built using 28nm technology on a comparative study basis for the purpose of marking out design trade-offs between performance and synthesized area.

## Slide 4: OBJECTIVE
Comprehension on a Hardware Device perspective through findings such as :
  Simulations Reports
  Synthesis Reports
  Implementation Reports.
Ease of Access of tools such as Xilinx Vivado and Intel Quartus Prime:
  Timing Analysis.
  Power Analysis.
Guiding engineers and researchers for the future development of classical MIPS to realize the superior system for next-generation wearable devices through this paper.

## Slide 5: INTRODUCTION
Moore’s Law & Chip-Manufacturing Trends.
Focus on Two Devices:
  Xilinx’ Gen-IV 28nm ASMBL 7-Series FPGA.
    Four 6-input Look Up Tables (LUTs) followed by Eight Registers within a slice inside a Configurable Logic Block (CLB)
  Intel’s 28nm ALM Cyclone – V E FPGA.
  8-input fracturable Adaptive LUT (ALUT) with Four Registers inside a CLB also known as a Logic Array Block (LAB) capable of achieving higher design packing capability
Wearable applications: Peripheral functionalities like wireless communications, image perception and display.

## Slide 6: System Architecture
A 32- Bit Microprocessor without Interlocked Pipelined Stages (MIPS) with 32-Bit Data Word, 32-Bit Addresses & 32-Bit Instructions of three types:
R – Type (Register)
I – Type (Immediate)
J – Type (Jump)
Where in, all Operation Codes (OP) are 6-Bits and all register addresses are 5-Bits.

## Slide 7: System Architecture
  Instruction Set Architecture (ISA)
Using General – Purpose Registers, the MIPS is designed with a five – stage RISC Load – Store Architecture, stages are:
Instruction Fetch (IF): Get Instruction from Memory, followed by Increment of the Program Counter (PC).
Instruction Decode (ID): Translates OP into control signals and register reads.
Execute (EX): Arithmetic Logic Unit (ALU) Operations, computing Jump or Branch to target operations.
Memory (MEM): Access Memory, if needed.
Writeback (WB): Updates Register / Memory File

## Slide 8: System Architecture
  This MIPS Architecture is developed with two addressing modes, displacement and immediate in nature with support of integers and IEEE – 754 floating-point numbers. MIPS also has a separate comparison and branching instruction
Format | BITS 31 – 26 | BITS 25 – 21 | BITS 20 – 16 | BITS 15 – 11 | BITS 10 – 6 | BITS 5 – 0
R | OP | Source Reg [0] | Source Reg [1] | Reg. Target | Shift Amt. | Function
I | OP | Source Reg [0] | Source Reg [1] | Immediate – 16 Bits |  | 
J | OP | Target – 26 Bits |  |  |  | 
Table I: MIPS Instruction Set Format

## Slide 9: System Architecture
  Register Transfer Level (RTL) Design
Expressing the ISA in a Register Transfer Level (RTL) format with required Datapath components and interconnections. Control signals for enabling Datapath elements to execute an instruction in the appropriate sequence through the design of a control logic. To manage hazards for smooth operation of the MIPS, a few units are added as mentioned below:
Forwarding Unit: Designed to forward the right output of the ALU, when data hazards are detected at the source registers of the current instruction.
Stall Control Unit: At the ID Stage, when the destination register of the current instruction is similar to the source registers, with the exceptions for load (LW) and XOR-Immediate (XORI), stalling of one clock cycle is required to resolve the caused data hazard.
Flush Control Unit: Designed to resolve control hazards, which performs actions to discard instructions in the IF and ID stages for J – Type Instructions.
Write-Back Forwarding Unit: When reading and writing of the same address causes hazards as the readout data may not be the right write data. This hazard is resolved by directly forwarding the correct writing data to the output.

## Slide 10: System Architecture
  Register Transfer Level (RTL) Design
Fig. 1: Register Transfer Level Elaborated Schematic Diagram

## Slide 11: System Architecture
  Integrated Circuit – Floorplanning Design
  Physical Design of Integrated Circuit (IC) chips into considering which part of device must remain static and which other parts of the device must be dynamic in nature.
  Timing Closure and Power Optimization are vital constraints to keep in mind during layout of Physical-Blocks (PBlocks), post – initial implementation of the design [6].
  Post RTL Design and elaboration, Input-Output (I/O) Pin Planning is carried out. During Floor planning, after an initial implementation, laying out of Auto-PBlocks of greater than 100 leaf cells are given top priority for five such – instance

## Slide 12: Hardware Design and Development
  In Xilinx Vivado and Intel Quartus Prime Lite, the project flow is almost similar post RTL Elaboration of the Design when it comes to pin and timing constraints.
  However, significantly different approaches are taken by the respective engines towards synthesis and implementation
  The Given instruction is converted to binary data and passed onto via $readmemb command into the processor.

## Slide 13: Simulation Analysis
Fig. 2: Post - Implementation Timing Waveform - Spartan 07

## Slide 14: Simulation Analysis
  Design Analysis & Synthesis
  With the Xilinx Vivado Synthesis Engine strategy set as Flow-Area Optimized: High which performs general area optimizations including changing the threshold for control set optimizations, forcing ternary adder implementations, applying lower thresholds for use of carry chain in comparators and also optimized multiplexer placements.
  When compared to a Synthesis Engine Setting of Flow-Performance Optimized: High where resource sharing is turned off, LUT combining is disabled and Shift-Register LUT (SRL) are inferred with a larger threshold, which focusses on synthesizing higher performance trading – off with larger area utilization.
  Although on Intel Quartus Prime Lite’s Quartus-Syn synthesis engine generates advanced hierarchical database with preservation of post-synthesis optimizations without impacting of previous partition placement or routing.

## Slide 15: Simulation Analysis
  Design Analysis & Synthesis
  The engine is on an overall optimized for better performance, although the default balanced strategy is also recommended keeping in mind routability, power consumption and compilation time.
  Enabling state – machine inferences is also used to improve the performance of the design.
  The compiler specifically targets strategies to reduce area utilization and trades-off with improved performance. If this, setting is set to off, the compiler extracts state – machines to optimize as regular logic

## Slide 16: Simulation Analysis
  Timing Closure and Pin Planning
Fig.3: Spartan – 07 Device Pinout Diagram
Fig.4: Cyclone V E Device Pinout Diagram

## Slide 17: Simulation Analysis
  Implementation & Fitter Process
Process | LUTs | Flip Flops | Total Power
Synthesis | 16,393 | 9,079 | 0.321 W
Implementation | 16,370 | 9,079 | 0.467 W
Process | ALMs | ALUTs | Registers
Synthesis | 21,874 | 24,846 | 8,960
Fitter | 19,734 | 24,847 | 9,161
Table II: Resource Utilizations - Spartan 07
Table III: Resource Utilization - Cyclone V E

## Slide 18: Simulation Analysis
Fig. 5: Implemented Package Diagram – Spartan 07
Fig. 6: Fitted Package Diagram – Cyclone V E

## Slide 19: Simulation Analysis
Fig.7: On-Chip Power Analysis XC7S100-676FGGA-2

## Slide 20: Simulation Analysis
Fig. 8: XADC Monitor Dashboard – Spartan 07 SP701 Evaluation Board

## Slide 21: Conclusion and Future Scope
  Conclusion
Miniaturization of core-intelligent devices capable of parallel processing with highly-pipelined architecture that are optimized to handle CPU-intensive operations enabling scalable high throughput applications with higher-bandwidth.
Nokia Wrist - Attached Sensor Platform (NWSP) is one example of a first generation high – density FPGA device applications for wearables with various drawbacks in terms of overall-device size and large power – consumption and leakage currents [7].
The MicroWIP325 is designed to overcome all of these disadvantages with the current technology we have at hand. Application-Specific Integrated Circuit (ASIC) Implementation and Fabrication of the MicroWIP325 design would enhance power and size reduction even further.

## Slide 22: Conclusion and Future Scope
  Conclusion
  The LUTs utilized post – implementation / fitter by the Cyclone V E is higher by 34.11% in comparison to the Spartan – 07 FPGA in spite the fact that the Cyclone V E FPGA has higher input LUTs in a CLB, thus increasing the utilized area.
  The synthesis and implementation engine strategy approaches of these two chip Original Equipment Manufacturers (OEM) vary widely. The end goal is essentially similar.
  The approach taken in this paper for Xilinx FPGA synthesis and implementation is area-optimization followed by performance-improvisation respectively.
  Whereas the approach is vice-versa for Intel FPGA synthesis and implementation. Xilinx FPGAs are also cost-effective on a head-to-head comparison with Intel FPGAs, although this depends on market scenarios given the fact about the current semi-conductor chip shortage crisis.

## Slide 23: Conclusion and Future Scope
  Future Scope
This design has been exported into a soft-core Intellectual Property (IP) MIPS processor, which can be efficient in terms of design modularity and reuse.
Xilinx Vivado IP Packager generates the soft-core IP configuration from the developed model rendering faster product design lifecycles.
Memory & Instruction files can be embedded into the processor based upon the goals and needs of the user.
Double-Issue Datapath Architecture would be an upgrade to the implementation in execution of instructions at nearly half the number of clock cycles required by the current architecture, however it would increase the number of current resources utilized [8].

## Slide 24: Conclusion and Future Scope
  Future Scope
Partial Reconfigurability of the FPGA, where in a portion of the FPGA functions on the tasks, whereas the other segment reconfigures itself based upon the need for extensive computing activities.
Although the power consumed by the device is in the range of 0.4W – 0.6W, the battery management system for the integrated control chip and the peripherals would be a Research and Development (R&D) task at hand, keeping in mind the compact nature of the target device.

## Slide 25: References
Xin Wu and Prabhuram Gopalan, “Xilinx Next Generation 28 nm FPGA Technology Overview,” WP312 (v1.1.1), Xilinx Inc., July 23, 2013.
Nick Mehta, “Xilinx 7 Series FPGAs: The Logical Advantage,” WP405 (v1.0), Xilinx Inc., March 06, 2012.
Altera Inc, “Cyclone V Device Handbook: Volume 1: Device Overview and Datasheet,” CV-5V1-1.2, February 2012.
S. S. Omran and A. K. Abdul-abbas, "Design and implementation of 32-Bits MIPS processor to Perform QRD Based on FPGA," 2018 International Conference on Engineering Technology and their Applications (IICETA), 2018, pp. 36-41, doi: 10.1109/IICETA.2018.8458073.
S. S. Omran and L. F. Jumma, "Design of SHA-1 & SHA-2 MIPS processor using FPGA," 2017 Annual Conference on New Trends in Information & Communications Technology Applications (NTICT), 2017, pp. 268-273, doi: 10.1109/NTICT.2017.7976113.
Xilinx Inc, “Floorplanning Methodology Guide,” UG633 (v14.5), April 10, 2013.
T. Ahola, P. Korpinen, J. Rakkola, T. Ramo, J. Salminen and J. Savolainen, "Wearable FPGA Based Wireless Sensor Platform," 2007 29th Annual International Conference of the IEEE Engineering in Medicine and Biology Society, 2007, pp. 2288-2291, doi: 10.1109/IEMBS.2007.4352782.
Tyson, A. L. Romas, S. Intan P and T. Adiono, "A pipelined double-issue MIPS based processor architecture," 2009 International Symposium on Intelligent Signal Processing and Communication Systems (ISPACS), 2009, pp. 583-586, doi: 10.1109/ISPACS.2009.5383771.
ELMO – Miniaturising Electronics 2002–2005”, Tekes Technology Programme Reports, 3/2006, ISBN 952-457-223-0,
http://www.tekes.fi/julkaisut/ELMO.pdf.